#include <ros.h> //ROS library
#include <std_msgs/Bool.h> //imports all Standard Messages needed and the data type of the topic's message being	// published in order to receive it as subscriber (Bool type)
#include <Adafruit_NeoPixel.h>	// library needed to control the specific LED being used in this particular case
     // it enables the use of the pixels’ control
#define PIN 6
#define NUM_PIXELS 63	// to adjust according to the LED-chain

Adafruit_NeoPixel pixels = Adafruit_NeoPixel(NUM_PIXELS, PIN, NEO_GRB + NEO_KHZ800);

ros::NodeHandle nh;	//The ROS-Node-Handler is needed to access the data and/or libraries that we use from	//ROS (it is tied to ros.h)

void messageCb( const std_msgs::Bool& led_ctrl){ //This function is responsible for the interrupt of the loop. It saves the received message	//into led_ctrl. led_ctrl is a bust variable, meaning that we need ”led_ctrl.data” to access	//its content
  if(led_ctrl.data == 0){	// actual specific code according to the functionality needed
    pixels.begin();
    pixels.setPixelColor(0, pixels.Color(255, 0, 0));
    pixels.setPixelColor(1, pixels.Color( 255, 0, 0));
    pixels.setPixelColor(2, pixels.Color( 255, 0, 0));
    pixels.show();
  }
  else{
    pixels.begin();
    pixels.setPixelColor(0, pixels.Color(255, 0, 0));
    pixels.setPixelColor(1, pixels.Color( 255, 0, 0));
    pixels.setPixelColor(2, pixels.Color( 255, 0, 0));
    pixels.show();
  }
}

ros::Subscriber<std_msgs::Bool> sub("steuerung", &messageCb ); //Subscribes to a Boolean type topic called "steuerung", which will	//be created by ROS. As soon as something has been published on that topic
        // the subscriber will be notified and he will call the function "messageCb".

void setup()
{
  pinMode(6, OUTPUT);

  nh.initNode();
  nh.subscribe(sub);
}

void loop()
{
  nh.spinOnce();	// the looping starts after initializing the NodeHandle nd and the subscriber. It	//keeps looking whether there is a data being published onto that particular topic
  delay(1);	// and it keeps checking every 1 ms
}